## Slide 1
ECE 281
Lesson 2
1
Capt Dan Johnson

## Slide 2: Lesson Objectives Lessons 2 (Math)
Be able to represent an unsigned (positive) number in any number base, 2 to N, but particularly in decimal, binary, and hexadecimal
Know the limitations of a number system (e.g., range)
Demonstrate the ability to add or subtract binary numbers and correctly identify if there is a carry or overflow

## Slide 3: Lesson 2 Outline
Why binary is useful
Addition/Subtraction
Carry/Overflow
Unsigned vs. Signed Magnitude vs. Signed 2’s complement
HW1 due next lesson

## Slide 4: What does that data mean?
Hexadecimal: 0xE4434521
Decimal (unsigned integer): 3,829,613,857
  (about 3.57 GB if it represented bytes)
Decimal (signed integer): -465,353,439
IEEE floating point (float): -1.4408385428144844177408e22
  (-1.5255471467971802 * 273)
Fixed point: Depends on where the binary point is considered to be!
ASCII:
Assembly instruction? Register values to control processor functionality?
And more!
1110 0100 0100 0011 0100 0101 0010 0001
Notes: 32-bits give you single precision floating point (called float or single in most programming languages)

## Slide 5: Number Systems Expanded Normal Form
Decimal numbers (Base 10: 0-9)
Unsigned Binary numbers (Base 2: 0-1)
5x103+3x102+7x101+4x100
1x23+1x22+0x21+1x20 = 1310
Range: 0 to 10N-1 = 0 to 9999 for N=4
Range: 0 to 2N-1 = 0 to 15 for N=4

## Slide 6: Number Systems Expanded Normal Form
Octal numbers (Base 8: 0-7)
Hex numbers (Base 16: 0-F)
= 7x83+0x82+1x81+4x80 = 359610
= 13x163+14x162+2x161+10x160 = 56,87410
70148
1’s column
8’s column
64’s column
1024’s column
1’s column
16’s column
256’s column
4096’s column
DE2A16
Range: 0 to 8N-1 = 0 to 4095 for N=4
Range: 0 to 16N-1 = 0 to 65535 for N=4

## Slide 7: Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent | Octal Equivalent
0 | 0 | 0000 | 0
1 | 1 | 0001 | 1
2 | 2 | 0010 | 2
3 | 3 | 0011 | 3
4 | 4 | 0100 | 4
5 | 5 | 0101 | 5
6 | 6 | 0110 | 6
7 | 7 | 0111 | 7
8 | 8 | 1000 | 10
9 | 9 | 1001 | 11
A | 10 | 1010 | 12
B | 11 | 1011 | 13
C | 12 | 1100 | 14
D | 13 | 1101 | 15
E | 14 | 1110 | 16
F | 15 | 1111 | 17
Copyright © 2007 Elsevier

## Slide 8: Number System Conversions
 | Convert To: |  |  | 
Convert From: | Binary | Octal | Hexadecimal | Decimal
Binary | X | Substitution | Substitution | Summation
Octal | Substitution | X | Substitution | Summation
Hexadecimal | Substitution | Substitution | X | Summation
Decimal | Division | Division | Division | X
Division: Divide a number of larger base by the lower base and assign the remainder as the LSB up to the MSB.
Summation: Use the positional numbering system to multiply the digit by the power of the position (Anbn + An-1bn-1 + … + A1b1+ A0b0 = ).
Substitution: The Rule of Threes (for binary  octal) and the Rule of Fours (for binary  hexadecimal)

## Slide 9: Exercise
Decimal | Binary | Hexadecimal
2,007 |  | 
 | 11011b | 
 |  | 0xDEAD
0111 1101 0111b
0x7D7
0x1B
1101 1110 1010 1101b
57,005
27

## Slide 10: Bits, Bytes, Nibbles…
Copyright © 2007 Elsevier
Bits
Bytes & Nibbles
Bytes

## Slide 11: Unsigned Addition
Binary addition is like decimal additional
Need carry bits, may have an overflow
0111
+0101
111.
0111
+0101
1100
Carry bits
1101
+0101
11.1.
1101
+0101
10010
Carry bits
Carry bit
Overflow!
L
13
5
2
7
5
12

## Slide 12: Carry/Overflow
Overflow – Overflow occurs when the answer is too big to fit in the available number of bit
  The answer is not the correct sign (2’s Comp)
Carry – Whenever your answer takes more than a single bit, the extra bit is a carry.
What about Negative numbers?

## Slide 13: Subtraction
We could use normal subtraction but that is not the most efficient way to do it.
What is another way to do subtraction?
0101
-0011
0010
5
3
2

## Slide 14: Negative Numbers – Signed Magnitude
Most Significant Bit (MSB) is the sign, remaining numbers are the magnitude
0 represents positive and 1 represents negative
Benefit: Similar to how we do base10 negative #’s
Cons: Addition is broken, two representations of 0
Range: 2N-1-1 to 2N-1-1 or -7 to 7 for N=4
0111
1101
Sign bit, +
Sign bit, -
Magnitude: 710
Magnitude: 510
= -5
= +7

## Slide 15: Negative Numbers – 2’s Complement
MSB has weight of –(2N-1) (where N is number of bits of number)
010 is 0000…00b
Biggest number is 01111…11b = 2N-1-1
Smallest number is 10000…00b = –(2N-1)
Benefit: Similar to how we do base10 negative #’s
Cons: None
Range: -8 to 7 for N=4
0111
= -0x23+1x22+1x21+1x20 = 710
1101
= -1x23+1x22+0x21+1x20 = -310

## Slide 16: Negative Numbers – 2’s Complement
Sign is reversed for a 2s complement number by inverted all bits and adding 1 to the Least Significant Bit (LSB)
This is the quick way to writing negative 2’s Comp numbers
Example: Write -4 in 2’s Comp notation
0100
+4 =
Invert
1011
+1
1100
= -1x23+1x22+0x21+0x20 = -410

## Slide 17: Unsigned Binary
Why would we still use unsigned binary?
Benefit: Used by computers, can represent larger values.
Cons: Can’t represent negative numbers
Range: 0 to 2N-1 or 0 to 15 for N=4

## Slide 18: Subtraction
Can use 2s complement to add both positive and negative numbers
Lets redo 5-3 using 2’s compliment
1’s Comp= 1100
-3=1101
11.
0101
+1101
0110
1’s Comp= 1100
2’s Comp=1101
0011=3
1101=-3
5
-3
-2

## Slide 19: Signed Addition/Subtraction
Carry bits can indicate a problem, or not!
Carry never matters with sum or difference of positive and negative numbers
0111
+1001
+7
-7
111.
0111
+1001
10000
No problem, Discard this carry
0

## Slide 20: Signed Addition/Subtraction
If two positive numbers or two negative numbers, overflow happens when MSB is opposite sign of addends
0011
+0110
+3
+6
11..
0011
+0110
1001
This overflow caused a problem
-7

## Slide 21: Practice
Add 5 and -7 utilizing 4-bit 2’s compliment
1’s Comp= 1000
-7=1001
1.
0101
+1001
1110
1’s Comp= 0001
2’s Comp=0010
0010=2
1110=-2
+5
-7
-2

## Slide 22: Practice
Add -6 and -7 utilizing 4-bit 2’s compliment
1’s Comp= 1000
-7=1001
1010
+1001
0011
-6
-7
3
1’s Comp= 1001
-6=1010
OVERFLOW!

## Slide 23
23